## Slide 1
Azure Chaos Studio Resilience Experiment
P087 | Resilience Engineering
Team T087
Skill Palaver Hackathon — Slot 1
Course: 24CC3046 — Microsoft Certified: Azure Administrator Associate
Team Members:
Gurrala Hareesh Reddy (2400090155) — Team Lead
Namathoti Nandu (2400090190)
Alamalakala Sneha (2400090174)
Rao Rupesh Sai (2400090150)
Room: R507A

## Slide 2
Problem Statement
Modern cloud applications must remain available during infrastructure failures
Challenge: Validate multi-zone architecture under zone-associated failure
Use cases: Inject zone failure, produce recovery evidence
Bottlenecks: Blast radius control, permissions setup
Service Continuity
Load Balancer
Failure

## Slide 3
Project Objectives
Build multi-zone Azure workload
Place behind Load Balancer
Prepare VMSS as Chaos Studio target
Design controlled VMSS shutdown experiment
Measure service behavior during failure
Success evidence: HTTP availability, instance state, and recovery state.

## Slide 4
Our Approach
Step 1: Deploy multi-zone VMSS
Step 2: Configure Load Balancer + health probe
Step 3: Deploy Nginx HTTP workload
Step 4: Onboard VMSS to Chaos Studio
Step 5: Validate failure/recovery behavior
Note: Chaos Studio deployment blocked by subscription policy; controlled VMSS failure used for validation.

## Slide 5
Azure Resilience Architecture
Architecture Overview:

## Slide 6
Infrastructure Implementation
Resource | Configuration
Resource Group | rg-t087-chaos-resilience
VM Scale Set | vmss-t087-chaos-resilience
Region | East Asia
Availability Zones | 1, 2, 3
Instances | 3
VM Size | Standard_B2ats_v2 (2 vCPU, 1 GiB RAM)
Load Balancer | lb-t087-chaos-resilience
Web Server | Nginx 1.24.0

## Slide 7
Traffic Flow and Health Detection
Traffic Path:
Client request
Public Load Balancer IP (20.239.17.139)
Load Balancer rule (TCP 80 → TCP 80)
Healthy VMSS backend instance
Nginx on port 80
Health Probe Configuration:
Protocol
HTTP
Port
80
Path
/

## Slide 8
Chaos Studio Target Configuration
Target Configuration:
Target: vmss-t087-chaos-resilience
Targeting Mode: Service-direct
Status: Enabled
Why Service-Direct Targeting:
Service-direct was used so the VMSS could be enabled as a Chaos Studio target without guest-agent setup.

## Slide 9
Planned Chaos Experiment Configuration
Experiment Name | exp-t087-zone-failure
Fault Type | VMSS Shutdown v2.0
Duration | 10 minutes
Abrupt Shutdown | False
Target | vmss-t087-chaos-resilience
Scope | Zone 1
Identity | System-assigned managed identity
Role | Azure built-in role (Virtual Machine Contributor)
Scoped to Zone 1 to limit blast radius. CONFIGURED/PLANNED — NOT EXECUTED

## Slide 10
Chaos Studio Deployment Constraint
Initiation
Start deployment request
Validation
Check region policy
Blocking
East US denied
Policy Details
Policy: Allowed resource deployment regions
Assignment: sys.regionrestriction
Attempted Location: East US
Effect: Deny
Environment constraint discovered during implementation, not a team failure.

## Slide 11
Controlled Failure Validation
Test methodology: Because Chaos Studio deployment was blocked by subscription policy, we validated resilience with a controlled VMSS instance failure.
01
Baseline
20 HTTP requests to Load Balancer IP
Result: 20/20 HTTP 200
02
Controlled Failure
Deallocated VMSS Instance 0 (Zone 1)
Command: az vmss deallocate --resource-group rg-t087-chaos-resilience --name vmss-t087-chaos-resilience --instance-ids 0
03
Traffic Validation During Failure
20 HTTP requests to Load Balancer IP
Result: 20/20 HTTP 200
04
Recovery
Started VMSS Instance 0
Result: All three instances running
05
Post-Recovery Validation
20 HTTP requests to Load Balancer IP
Result: 20/20 HTTP 200
Note: This simulates an instance-level failure, not an entire Azure availability zone failure.

## Slide 12
Experimental Results
Results Summary:
Test Stage | Infrastructure State | HTTP Result
Baseline | 3 instances running (Zones 1, 2, 3) | 20/20 HTTP 200
During Controlled Failure | Zone 1 instance deallocated; Zones 2 & 3 running | 20/20 HTTP 200
After Recovery | All 3 instances running (Zones 1, 2, 3) | 20/20 HTTP 200
Key Observation: The Load Balancer continued serving HTTP traffic when the Zone 1-associated VMSS instance was deallocated.
Note: These are 20 sampled HTTP requests per stage.

## Slide 13
What the Results Demonstrate
Key Findings:
Finding 1: Load Balancer Continuity
Load Balancer traffic continued during the Zone 1 VMSS deallocation.
Finding 2: Multi-Zone Redundancy
Zones 2 and 3 continued serving traffic without interruption.
Finding 3: Successful Recovery
The failed instance was restarted successfully with Azure CLI.
Finding 4: Post-Recovery Validation
Post-recovery testing again returned 20/20 HTTP 200 responses.
Conclusion:
The architecture demonstrated service continuity under the controlled instance-failure scenario.
Scope of Evidence:
This evidence applies to the controlled VMSS instance failure tested in this project and validates the multi-zone redundancy design at the VMSS instance level.
Note: This is a targeted test of the specific failure scenario, not a full SLA or all-zone resilience validation.

## Slide 14
Team Contributions
1
Gurrala Hareesh Reddy (2400090155)
Overall architecture and project coordination
Azure infrastructure design and resilience validation
Experiment planning and final integration
2
Namathoti Nandu (2400090190)
VMSS and Load Balancer deployment
Nginx configuration and health probe setup
Networking troubleshooting and validation
3
Alamalakala Sneha (2400090174)
Monitoring and evidence collection setup
Baseline/failure/recovery validation
HTTP test documentation and analysis
4
Rao Rupesh Sai (2400090150)
Chaos Studio investigation and research
Service-direct onboarding and configuration
Experiment design and policy investigation

## Slide 15
Conclusion & Next Step
Project Summary:
A three-zone VMSS architecture was implemented behind an Azure Load Balancer
Chaos Studio target onboarding was completed successfully
The planned VMSS Shutdown experiment was configured with controlled Zone 1 scope
20/20 sampled HTTP requests returned HTTP 200 during the tested failure
Recovery was verified after restarting the failed instance
Next Step:
Run the Chaos Studio experiment in a permitted environment or region.
Final Statement:
Controlled failure. Measured behavior. Evidence-based resilience validation.